## Slide 1: ECE408/CS483 Fall 2015 Applied Parallel Programming Lectures 5 and 6: Memory Model and Locality

## Slide 2: Programmer View of CUDA Memories
Each thread can:
  Read/write per-thread registers (~1 cycle)
  Read/write per-block shared memory (~5 cycles)
  Read/write per-grid global memory (~500 cycles)
  Read/only per-grid constant memory (~5 cycles with caching)
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 3: CUDA Variable Type Qualifiers
__device__ is optional when used with __shared__, or __constant__
Automatic variables without any qualifier reside in a register
  Except per-thread arrays that reside in global memory
Variable declaration | Memory | Scope | Lifetime
int LocalVar; | register | thread | thread
__device__ __shared__ int SharedVar; | shared | block | block
__device__ int GlobalVar; | global | grid | application
__device__ __constant__ int ConstantVar; | constant | grid | application

## Slide 4
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width)
{
__shared__ float subTileM[TILE_WIDTH][TILE_WIDTH];
__shared__ float subTileN[TILE_WIDTH][TILE_WIDTH];

## Slide 5: A Common Programming Strategy
Global memory resides in device memory (DRAM)
A profitable way of performing computation on the device is to tile the input data to take advantage of fast shared memory:
  Partition data into subsets that fit into shared memory
  Handle each data subset with one thread block by:
    Loading the subset from global memory to shared memory, using multiple threads to exploit memory-level parallelism
    Performing the computation on the subset from shared memory; each thread can efficiently multi-pass over any data element
    Copying results from shared memory to global memory

## Slide 6: Matrix-Matrix Multiplication using Shared Memory

## Slide 7: A Simple Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width)
{
// Calculate the row index of the P element and M
int Row = blockIdx.y * blockDim.y + threadIdx.y;
// Calculate the column index of P and N
int Col = blockIdx.x * blockDim.x + threadIdx.x;
if ((Row < Width) && (Col < Width)) {
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += M[Row*Width+k] * N[k*Width+Col];
P[Row*Width+Col] = Pvalue;
}
}

## Slide 8: How about performance?
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
All threads access global memory for their input matrix elements
  Two memory accesses (8 bytes) per floating point multiply-add
  4B/s of memory bandwidth/FLOPS
  4*1,000 = 4,000 GB/s required to achieve peak FLOP rating
  150 GB/s limits the code at 37.5 GFLOPS
The actual code runs at about 25 GFLOPS on Fermi
Need to drastically cut down memory accesses to get closer to the peak 1,000 GFLOPS

## Slide 9: Shared Memory Blocking Basic Idea
Thread 1
Thread 2
…
in
Global Memory
Thread 1
Thread 2
…
Global Memory
in
On-chip Memory

## Slide 10: Outline of Technique
Identify a block/tile of global data that are accessed by multiple threads
Load the block/tile from global memory into on-chip memory
Have the multiple threads to access their data from the on-chip memory
Move on to the next block/tile

## Slide 11: Idea: Use Shared Memory to reuse global memory data
Each input element is read by WIDTH threads.
Load each element into Shared Memory and have several threads use the local version to reduce the memory bandwidth
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
ty
tx

## Slide 12: Tiled Multiply
M
N
P
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Break up the execution of the kernel into phases so that the data accesses in each phase is focused on one subset (tile) of M and N

## Slide 13: Loading a Tile
All threads in a block participate
  Each thread loads one Md element and one Nd element in based tiled code
Assign the loaded element to each thread such that the accesses within each warp is coalesced (more later).

## Slide 14: Work for Block (0,0)
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1
SM
SM

## Slide 15: Work for Block (0,0)
SM
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1

## Slide 16: Work for Block (0,0)
SM
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1

## Slide 17: Work for Block (0,0)
N3,0
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,3
M0,2
M1,2
M1,3
N2,1
N2,0
N1,3
SM

## Slide 18: Work for Block (0,0)
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
SM
N3,0
M0,3
M0,2
M1,2
M1,3
N2,1
N2,0
N1,3

## Slide 19: Loading an Input Tile 0
M
N
P
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Accessing tile 0 2D indexing:
M[Row][tx]
N[ty][Col]

## Slide 20: Loading an Input Tile 1
M
N
P
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Accessing tile 1 in 2D indexing:
M[Row][1*TILE_WIDTH+tx]
N[1*TILE_WIDTH+ty][Col]

## Slide 21: Loading an Input Tile m
M
N
P
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
However, M and N are dynamically allocated and can only use 1D indexing:
M[Row][m*TILE_WIDTH+tx]
M[Row*Width + m*TILE_WIDTH + tx]
N[m*TILE_WIDTH+ty][Col]
N[(m*TILE_WIDTH+ty) * Width + Col]
m
m

## Slide 22: Barrier Synchronization
An API function call in CUDA
  __syncthreads()
All threads in the same block must reach the __syncthreads() before any can move on
Best used to coordinate tiled algorithms
  To ensure that all elements of a tile are loaded
  To ensure that all elements of a tile are consumed

## Slide 23
Figure 4.11 An example execution timing of barrier synchronization.
…
Thread 0
Thread 1
Thread 2
Thread 3
Thread 4
…
Thread N-3
Thread N-2
Thread N-1
Time

## Slide 24: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width)
{
1. __shared__ float subTileM[TILE_WIDTH][TILE_WIDTH];
2. __shared__ float subTileN[TILE_WIDTH][TILE_WIDTH];
3. int bx = blockIdx.x; int by = blockIdx.y;
4. int tx = threadIdx.x; int ty = threadIdx.y;
// Identify the row and column of the P element to work on
5. int Row = by * TILE_WIDTH + ty;
6. int Col = bx * TILE_WIDTH + tx;
7. float Pvalue = 0;
// Loop over the M and N tiles required to compute the P element
8. for (int m = 0; m < Width/TILE_WIDTH; ++m) {
// Collaborative loading of M and N tiles into shared memory
9. subTileM[ty][tx] = M[Row*Width + m*TILE_WIDTH+tx];
subTileN[ty][tx] = N[(m*TILE_WIDTH+ty)*Width+Col];
__syncthreads();
12. for (int k = 0; k < TILE_WIDTH; ++k)
13. Pvalue += subTileM[ty][k] * subTileN[k][tx];
14. __synchthreads();
15. }
16. P[Row*Width+Col] = Pvalue;
}

## Slide 25: Compare with Base Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width)
{
// Calculate the row index of the P element and M
int Row = blockIdx.y * blockDim.y + threadIdx.y;
// Calculate the column index of P and N
int Col = blockIdx.x * blockDim.x + threadIdx.x;
if ((Row < Width) && (Col < Width)) {
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += M[Row*Width+k] * N[k*Width+Col];
P[Row*Width+Col] = Pvalue;
}
}

## Slide 26: Shared Memory and Threading
Each SM in Maxwell has 64KB shared memory (48KB max per block)
  Shared memory size is implementation dependent!
  For TILE_WIDTH = 16, each thread block uses 2*256*4B = 2KB of shared memory.
  Can potentially have up to 32 Thread Blocks actively executing
    This allows up to 8*512 = 4,096 pending loads. (2 per thread, 256 threads per block)
  The next TILE_WIDTH 32 would lead to 2*32*32*4B= 8KB shared memory usage per thread block, allowing 8 thread blocks active at the same time
Using 16x16 tiling, we reduce the accesses to the global memory by a factor of 16
  The 150GB/s bandwidth can now support (150/4)*16 = 600 GFLOPS!

## Slide 27: Device Query
Number of devices in the system
    int dev_count;
    cudaGetDeviceCount( &dev_count);
Capability of devices
    cudaDeviceProp dev_prop;
    for (i = 0; i < dev_count; i++) {
    cudaGetDeviceProperties( &dev_prop, i);
// decide if device has sufficient resources and capabilities
    }
cudaDeviceProp is a built-in C structure type
  dev_prop.dev_prop.maxThreadsPerBlock
  Dev_prop.sharedMemoryPerBlock
  …

## Slide 28: Any more questions? Read Chapter 5!