## Slide 1: ECE408/CS483 Fall 2015 Applied Parallel Programming Lecture 7: DRAM Bandwidth

## Slide 2: Global Memory (DRAM) Bandwidth
Ideal
Reality

## Slide 3: DRAM Bank Organization
Each core array has about O(1M) bits
Each bit is stored in a tiny capacitor, made of one transistor
Memory Cell
Core Array
Row
Decoder
Sense Amps
Column Latches
Mux
Row
Addr
Column
Addr
Off-chip Data
Wide
Narrow
Pin Interface

## Slide 4: A very small (8x2 bit) DRAM Bank
decode
0
1
1
Sense amps
Mux

## Slide 5: DRAM core arrays are slow.
Reading from a cell in the core array is a very slow process
  DDR: Core speed = ½ interface speed
  DDR2/GDDR3: Core speed = ¼ interface speed
  DDR3/GDDR4: Core speed = ⅛ interface speed
  … likely to be worse in the future
decode
To sense amps
A very small capacitance that stores a data bit
About 1000 cells connected to each vertical line

## Slide 6: DRAM Bursting
decode
0
1
0
Sense amps
Mux

## Slide 7: DRAM Bursting
decode
0
1
1
Sense amps and buffer
Mux

## Slide 8: DRAM Bursting for the 8x2 Bank
time
Address bits to decoder
Core Array access delay
2 bits
to pin
2 bits
to pin
Non-burst timing
Burst timing
Modern DRAM systems are designed to be always accessed in burst mode. Burst bytes are transferred but discarded when accesses are not to sequential locations.

## Slide 9: Multiple DRAM Banks
decode
Sense amps
Mux
decode
Sense amps
Mux
0
1
1
0
Bank 0
Bank 1

## Slide 10: DRAM Bursting for the 8x2 Bank
time
Address bits to decoder
Core Array access delay
2 bits
to pin
2 bits
to pin
Single-Bank burst timing, dead time on interface
Multi-Bank burst timing, reduced dead time

## Slide 11: Placing a 2D C array into linear memory space
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
M1,3
M0,2
M0,1
M0,0
M0,3
M1,1
M1,0
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
M3,1
M3,0
M3,2
M3,3
M
linearized order in increasing address

## Slide 12: A Simple Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width)
{
// Calculate the row index of the P element and M
int Row = blockIdx.y * blockDim.y + threadIdx.y;
// Calculate the column index of P and N
int Col = blockIdx.x * blockDim.x + threadIdx.x;
if ((Row < Width) && (Col < Width)) {
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += M[Row*Width+k] * N[k*Width+Col];
P[Row*Width+Col] = Pvalue;
}
}

## Slide 13: Two Access Patterns
d_M
d_N
W
I
D
T
H
WIDTH
Thread 1
Thread 2
(a)
(b)
M[Row*Width+k]
N[k*Width+Col]
k is loop counter in the inner product loop of the kernel code

## Slide 14: N accesses are coalesced.
N
T0
T1
T2
T3
Load iteration 0
T0
T1
T2
T3
Load iteration 1
Access direction in Kernel code
…
N0,2
N1,1
N0,1
N0,0
N1,0
N0,3
N1,2
N1,3
N2,1
N2,0
N2,2
N2,3
N3,1
N3,0
N3,2
N3,3
N0,2
N0,1
N0,0
N0,3
N1,1
N1,0
N1,2
N1,3
N2,1
N2,0
N2,2
N2,3
N3,1
N3,0
N3,2
N3,3

## Slide 15: M accesses are not coalesced.
M
T0
T1
T2
T3
Load iteration 0
T0
T1
T2
T3
Load iteration 1
Access direction in Kernel code
…
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
M0,2
M0,1
M0,0
M0,3
M1,1
M1,0
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
M[Row*Width+k]

## Slide 16
d_M
d_N
W
I
D
T
H
WIDTH
d_M
d_N
Original
Access
Pattern
Tiled
Access
Pattern
Copy into
scratchpad
memory
Perform
multiplication
with scratchpad
values
Figure 6.10: Using shared memory to enable coalescing

## Slide 17: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width)
{
1. __shared__ float subTileM[TILE_WIDTH][TILE_WIDTH];
2. __shared__ float subTileN[TILE_WIDTH][TILE_WIDTH];
3. int bx = blockIdx.x; int by = blockIdx.y;
4. int tx = threadIdx.x; int ty = threadIdx.y;
// Identify the row and column of the P element to work on
5. int Row = by * TILE_WIDTH + ty;
6. int Col = bx * TILE_WIDTH + tx;
7. float Pvalue = 0;
// Loop over the M and N tiles required to compute the P element
8. for (int m = 0; m < Width/TILE_WIDTH; ++m) {
// Collaborative loading of M and N tiles into shared memory
9. subTileM[? ][? ] = M[ ? ];
subTileN[? ][? ] = N[ ? ];
__syncthreads();
12. for (int k = 0; k < TILE_WIDTH; ++k)
13. Pvalue += subTileM[ty][k] * subTileN[k][tx];
14. __synchthreads();
15. }
16. P[Row*Width+Col] = Pvalue;
}

## Slide 18: Any More Questions? Read Chapter 6